## Slide 1: Representation of trade and transportation networks in global energy models Updates: 2019-08-07
Jun Ukita Shepard
IIASA-YSSP 2019

## Slide 2: Updates
All energy commodities represented in trade technologies
  Crude oil, light oil, fuel oil, LNG, coal
Shipping technologies parameterized
Scenarios developed:
  High tariff, low tariff
  NAM-CPA sanction
  LNG/electricity-fueled shipping becomes cost competitive by 2100
Run scenarios and compare

## Slide 3: Regional specification

## Slide 4: Representing shipping in MESSAGE Global pool of shipping capacity
Legend:
Level (e.g. primary)
Node (e.g. R14_RUS)
Commodity (e.g. crude oil)
Technology (e.g. oil_exp)
Parameter (e.g. input)
liquid_shipping_capacity
fueloil
liquid_shipping
AFR
Input
Output
SECONDARY
GLB
node_loc
AFR
EXPORT

## Slide 5: Shipping technology specification Historical activity
UNCTAD has global historical activity in billion tonnes-km (2000-2018)
UNCTAD has activity in million tonnes disaggregated by region for 2006-2017
Take share of region activity in million tonnes to disaggregate global historical activity

## Slide 6: Shipping technology specification Investment cost
Type of shipping |  | Fuel input (kg/bton-km-y) |  |  | Captial cost |  |  | Assumptions |  |  |  | 
 | Type of fuel | By weight (kg/bton-km-y) | By energy (GWa/bton-km-y) | Emissions factor (Mt/bton-km-y) | Overnight cost ($M) | Annualized, 10%DR ($M/y) | Annualized ($M/bton-km-y) | DWT (ton) | Annual distance (10^9km/y) | Number of ships | Average payload per ship (bton-km/y) | Average distance traveled (km/y)
Liquid | Diesel | 6894865.04 | 0.01 | 0.02 | 76.00 | 8.37 | 6.24 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Liquid | LNG | 3678751.33 | 0.00 | 0.01 | 96.00 | 10.58 | 7.88 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Liquid | Electricity | NA | 0.00 | 0.00 | 192000.00 | 21152.27 | 15758.19 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | Diesel | 7283748.84 | 0.01 | 0.02 | 51.60 | 5.68 | 4.24 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | LNG | 3052216.32 | 0.00 | 0.01 | 71.60 | 7.89 | 5.88 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | Electricity | NA | 0.00 | 0.00 | 1432000.00 | 157760.68 | 117529.83 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | Diesel | 16810656.90 | 0.02 | 0.05 | 180.00 | 19.83 | 14.77 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | LNG | 5594115.78 | 0.01 | 0.01 | 200.00 | 22.03 | 16.41 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | Electricity | NA | 0.00 | 0.00 | 4000000.00 | 440672.29 | 328295.62 | 100000 | 5.05 | 376219 | 1.34 | 13423.03

## Slide 7: Shipping relation specification
Add relation parameters:
includes crude oil, light oil, fuel oil; includes coal, includes LNG
includes diesel (fuel oil), LNG, electricity as fuel inputs

## Slide 8: Scenarios
Baseline, global schema
Baseline, bilateral schema (distance only)
Baseline, distance and tariffs
High tariffs
Low tariffs
NAM-CPA sanction
LNG/Electric shipping cost-competitive by 2100

## Slide 9: Compare global schema to bilateral schema Crude oil imports

## Slide 10: Compare global schema to bilateral schema Light oil imports

## Slide 11: Compare global schema to bilateral schema Fuel oil imports

## Slide 12: Compare global schema to bilateral schema Coal imports

## Slide 13: Compare global schema to bilateral schema LNG imports

## Slide 14: Compare global schema to bilateral schema Crude oil exports

## Slide 15: Compare global schema to bilateral schema Light oil exports

## Slide 16: Compare global schema to bilateral schema Fuel oil exports

## Slide 17: Compare global schema to bilateral schema Coal exports

## Slide 18: Compare global schema to bilateral schema LNG exports