## Slide 1: Representation of trade and transportation networks in global energy models Updates: 2019-08-07
Jun Ukita Shepard
IIASA-YSSP 2019

## Slide 2: Updates
All energy commodities represented in trade technologies
  Crude oil, light oil, fuel oil, LNG, coal
Shipping technologies parameterized
Scenarios developed:
  High tariff, low tariff
  NAM-CPA sanction
  LNG/electricity-fueled shipping becomes cost competitive by 2100
Run scenarios and compare

## Slide 3: Regional specification

## Slide 4: Representing shipping in MESSAGE Global pool of shipping capacity
Legend:
Level (e.g. primary)
Node (e.g. R14_RUS)
Commodity (e.g. crude oil)
Technology (e.g. oil_exp)
Parameter (e.g. input)
liquid_shipping_capacity
fueloil
liquid_shipping
AFR
Input
Output
SECONDARY
GLB
node_loc
AFR
EXPORT

## Slide 5: Shipping technology specification Historical activity
UNCTAD has global historical activity in billion tonnes-km (2000-2018)
UNCTAD has activity in million tonnes disaggregated by region for 2006-2017
Take share of region activity in million tonnes to disaggregate global historical activity

## Slide 6: Shipping technology specification Investment cost
Type of shipping |  | Fuel input (kg/bton-km-y) |  |  | Captial cost |  |  | Assumptions |  |  |  | 
 | Type of fuel | By weight (kg/bton-km-y) | By energy (GWa/bton-km-y) | Emissions factor (Mt/bton-km-y) | Overnight cost ($M) | Annualized, 10%DR ($M/y) | Annualized ($M/bton-km-y) | DWT (ton) | Annual distance (10^9km/y) | Number of ships | Average payload per ship (bton-km/y) | Average distance traveled (km/y)
Liquid | Diesel | 6894865.04 | 0.01 | 0.02 | 76.00 | 8.37 | 6.24 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Liquid | LNG | 3678751.33 | 0.00 | 0.01 | 96.00 | 10.58 | 7.88 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Liquid | Electricity | NA | 0.00 | 0.00 | 192000.00 | 21152.27 | 15758.19 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | Diesel | 7283748.84 | 0.01 | 0.02 | 51.60 | 5.68 | 4.24 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | LNG | 3052216.32 | 0.00 | 0.01 | 71.60 | 7.89 | 5.88 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
Solid | Electricity | NA | 0.00 | 0.00 | 1432000.00 | 157760.68 | 117529.83 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | Diesel | 16810656.90 | 0.02 | 0.05 | 180.00 | 19.83 | 14.77 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | LNG | 5594115.78 | 0.01 | 0.01 | 200.00 | 22.03 | 16.41 | 100000 | 5.05 | 376219 | 1.34 | 13423.03
LNG | Electricity | NA | 0.00 | 0.00 | 4000000.00 | 440672.29 | 328295.62 | 100000 | 5.05 | 376219 | 1.34 | 13423.03

## Slide 7: Shipping relation specification
Add relation parameters:
includes crude oil, light oil, fuel oil; includes coal, includes LNG
includes diesel (fuel oil), LNG, electricity as fuel inputs

## Slide 8: Scenarios
Baseline, global schema
Baseline, bilateral schema (distance only)
Baseline, distance and tariffs
High tariffs
Low tariffs
NAM-CPA sanction
LNG/Electric shipping cost-competitive by 2100
Carbon emissions capped at 1000Gt, cumulative

## Slide 9: Building scenarios Tariffs
Use historical import tariff rates on primary products
  Aggregate to MESSAGE region
  High tariffs = tariffs are 1000% historical median by 2030
  Low tariffs = tariffs are -1000% of historical median by 2030
Apply to historical import prices, derived from trade data
Apply to the variable cost parameter (var_cost) for import technologies

## Slide 10: Building scenarios Historical Tariff Rates

## Slide 11: Building scenarios Scenario Tariff Rates

## Slide 12: Building scenarios Sanctions
Run baseline scenario
Based on activity, generate indicators for embodied sanction
  Example:
    NAM and CPA apply sanctions to each other
    LAM trades with NAM in year 2020
    LAM will be in “embodied sanction” with CPA in year 2020
    If LAM trades with both NAM and CPA, whichever activity is greater
  If in embodied sanction, variable cost goes up 30%
  If in total sanction, variable cost goes up to 10 times maximum (prohibitive)

## Slide 13: Tableau Workbooks
Compare sanction scenarios: https://public.tableau.com/profile/jun.shepard#!/vizhome/model_trade_paths/CompareSanctions?publish=yes
Compare tariff scenarios:
https://public.tableau.com/profile/jun.shepard#!/vizhome/model_trade_paths/Comparetariff?publish=yes
Compare CO2 bound scenario:
https://public.tableau.com/profile/jun.shepard#!/vizhome/model_trade_paths/CompareCO2?publish=yes

## Slide 14: Total carbon emissions, by scenario Difference from baseline

## Slide 15: Total System Cost System cost by scenario

## Slide 16: Compare global schema to bilateral schema Crude oil imports

## Slide 17: Compare global schema to bilateral schema Light oil imports

## Slide 18: Compare global schema to bilateral schema Fuel oil imports

## Slide 19: Compare global schema to bilateral schema Coal imports

## Slide 20: Compare global schema to bilateral schema LNG imports

## Slide 21: Compare global schema to bilateral schema Crude oil exports

## Slide 22: Compare global schema to bilateral schema Light oil exports

## Slide 23: Compare global schema to bilateral schema Fuel oil exports

## Slide 24: Compare global schema to bilateral schema Coal exports

## Slide 25: Compare global schema to bilateral schema LNG exports