## Slide 1: Representation of trade and transportation networks in global energy models Updates: 2019-06-18
Jun Ukita Shepard
IIASA-YSSP 2019

## Slide 2: Updates
Data validation
  Update heating values to IEA-published values
  Validation looks OK
Mapping shortest paths
  Made flexible shortest path algorithm
  Link shortest path to trade values for regional aggregation (flexible)
MESSAGE review

## Slide 3: Shortest path algorithm
User inputs:
Seaports of interest (csv file)
Level of node granularity (value)
Regional specification (csv file)
Step 1: Node definition
Step 2: Calculate distance
Step 3: Floyd-Warshall Algorithm
Step 4: Link to trade data
Step 5: Assign trade to port
Step 6: Calculate total trade to/from port
Step 7: Calculate share of imports/exports by region
Step 8: Identify primary ports by region

## Slide 4: Shortest path algorithm (detailed)
User inputs:
Seaports of interest (csv file)
Level of node granularity (value)
Regional specification (csv file)
Step 1: Node definition
Define nodes (ports + uniform nodes)
Generate combinations of all defined nodes
Step 2: Calculate distance
Calculate Haversine distance between nodes
Put distance into matrix
Step 3: Floyd-Warshall Algorithm
Run FW algorithm for shortest route between ports
There can be multiple ports per country (e.g. USA)
For each country-country pair (, ) identify port-port pair that is shortest distance ()
Step 4: Link to trade data
For each energy commodity , assign trade amount in year ()
Step 5: Assign trade to port
For each commodity :
Assign trade amount in year ( for imports, for exports) to each port-port combination
Step 6: Calculate total trade to/from port
For each commodity :
Sum and for each port () in a region ( and )
Step 7: Calculate share of imports/exports by region
For each region :
Calculate share of commodity moving to each port in :
Calculate share of commodity moving from each port in :
Step 8: Identify primary ports by region
For each region :
The port with the largest and are the primary import/export port for region in year for commodity